Flowbits - rectangular blocks that can be connected together to form circuits.

(TODO: Better name?)

Basic concepts

- Blocks attach to each other with magnets.  Power lines are on top of magnets.

- There is one power block that supplies power.

- The signal is transmitted digitally between each block (using IR light).

- Each block typically has one output signal that it broadcasts to all neighbors, and uses the neighbors output signals for some of its parameters.

- There is one generic computational block that can be set to different modes / functions.

- There might also be other types of blocks eventually¸ e.g. sensor blocks, motor blocks, tentacle blocks, light driver blocks, wall power remote control blocks, etc..

- Dimensions of block probably around 7x7 to 8x8 cm, leaves room for 4xAA battery case and fits nicely in hand.

  - Rectangular grid allows for double sized or odd sized blocks too (e.g. one to two octave piano keyboard block).

Blocks

Powerblock

- 4xAA battery holder

- DC 5V input jack

- PWM output drivers x 6 (one for each edge, encode value to 0..full output cycle)

- Servo outputs x 6 (one for each edge, encode incoming edge value to servo position

- (Power switch)

- Builtin speaker would be nice too.

Sensor Block

General computation block

- ATMega microcontroller, 4 RGB leds, potentiometer for navigation and parameter adjustment, 4 clickable edges, 2x7 segment led screen

- Each mode has a number of parameters, whose values can be set with the rotating wheel to a specific value, or to the (average) value of specified neighbor output(s), or maybe to more complex functions (simple signal / noise generators)

- Available modes (followed by parameters for the mode):

  - Signal generator

    - Waveform

      - Sine, Square, Sawtooth, etc

    - Frequency

    - Amplitude

  - Noise generator

  - Sequencer

  - Random melody / sequence generator

  - Mixer

  - Filter

  - Delay filter (echo, reverb, etc effects)

  - RGB signal visualizator

  - Neural network / game of life nodes (4 of them, one for each side)

  - etc

Part list (for general computation block):

- Rotary encoder x1

  - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=987-1398-ND

  - 10 pcs: 0.93900 / a

- Microcontroller x1

  - ATMega 328 PU

    - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=ATMEGA328-PU-ND

    - 3.05  (25 pieces: 1.91 / a)

  - or AT90USB162 (builtin usb support, surface mount)

    - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=AT90USB162-16AU-ND

    - 2.88 (25 pieces: 1.8 / a)

- Resonator 16 Mhz x1

  - Digikey

    - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=490-1214-ND

    - 10 pcs: 0.399 / a

  - Futurlec

    - http://www.futurlec.com/Crystals/RESON16M0P3pr.shtml

    - 0.2 / a

- Capacitors x2

  - Filter caps for microcontroller

    - (Close to zero, already have)

  - Power cap for scratchy contact

    - 47uF or similar electrolyte

- Protection diode for power polarity

  - ~0.5 - 1 A @ 6V

- Resistors

  - Series resistors for RGB lights, LED segment display..

    - LED Segment display: 14 (or 16) resistors

    - RGB Leds: 12 resistors

    - Maybe use resistor networks for saved space and improved sanity

    - Resistor network, 7 resitors, 8 pin, 220 Ohm: (maybe a bit too expensive)

      - Digikey

        - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=4608X-1-221LF-ND

        - 0.25 / a when 50+

      - Futurlec

        - http://www.futurlec.com/ResNetworks.shtml

        - 220ohm 9 Resistor Network (10 pins)

        - 0.25 / a

  - Combination resistors for tilt switch, 4 of different unique values (high accuracy, we'll get 16 different values that we need to differentiate after A/D)

- IR Leds, 940 nm, 3mm x4

  - Digikey

    - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=754-1241-ND

    - 0.11 / a when 25+

  - Futurlec

    - http://www.futurlec.com/LED/INF3940pr.shtml

    - 0.13 / a when 25+

- IR transistors 940nm x4

  - Digikey

    - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=1080-1158-ND

    - 0.21 / a when 10+

  - Futurlec

    - http://www.futurlec.com/LED/INFD3940TRANSpr.shtml

    - 0.15 a

- RGB Leds, common anode, diffuse x4

  - 0.25 / a from ebay seller for 100+

- Tactile swithces x 4

  - http://search.digikey.com/scripts/DkSearch/dksus.dll?Detail&name=450-1650-ND

  - 0.056 / a when 50+

- LED Dual 7 Segment screen x1

  - Futurlec

    - http://www.futurlec.com/LED/7DR5621BSpr.shtml

    - 0.75 / a when under 25

- Magnets x 8

  - http://www.dealextreme.com/p/super-strong-rare-earth-square-re-magnets-100-pack-51744

  - 0.144 / a when 100+

    - Tilattu

- Plastic cover material - diffuse, translucent white or darker plastic, preferably something not as brittle as acrylic

- Plastic case, 3D printed?

- PCB (smaller than total footprint)

- Programming header?

- Shift register, 74HC595 x2

  - Through hole

    - http://www.futurlec.com/74HC/74HC595pr.shtml

    - $0.5

    - $0.42 when 25+

    - $0.35 when 100+

  - SMD version (SOIC)

    - http://www.futurlec.com/74HC/74HC595SMDpr.shtml

    - $0.15

Parts to be ordered from three sources, digikey, futurlec, and dealextreme + 3D printed case.  Maybe ponocos german partner for a lasercut top surface ~2€ /a when ordering 25.

Cost: 8.86 + case plastic, pcb etc -> ~10$(+)

TODO: LEDs need sources and sink capable of driving them, atmega only supports max 25-30mA per pin, and max 110mA total.

Need 4 sinks for

- 3 RGB channels

- 1 x 4 IR sender leds (one channel) (could also be source-driven)

Need 6 sources for

- 2 (or 3) led segment displays (selecting character to light up)

- 4 RGB Leds, for selecting directions to light up

7 darlington transistors sink

- http://www.futurlec.com/Linear/ULN2003Apr.shtml

  - $0.3 / a for 25+

- http://www.futurlec.com/Linear/MC1413Ppr.shtml

  - $0.26 / a for 25+

Single PNP transistor

- http://www.futurlec.com/Transistors/PN2907Apr.shtml

  - 0.6A, 500mW dissipation, high gain.

  - $0.04 / a for 100+

  - Most widely used, so use this by default

- http://futurlec.com/Transistors/MPS2907Apr.shtml

  - $0.04 / a for 100+

- http://futurlec.com/Transistors/2SA1515pr.shtml

  - $0.04 / a for 100+

We have two reels (~4k pcs) of PNP SMD transistors (100mA) at the lab.


Single NPN sink transistor

- http://futurlec.com/Transistors/KTC3203pr.shtml

- ~$0.04 / a for 100+

- Not very common, but available from futurlec.  Substitutable with any NPN transistor with hfe > 100, voltage 20+, and currect handling of more than 500mA

metal strip for holding magnets (thin copper?)

- or trap them in a wire loop?

-> About $0.05 per source or sink -> + $0.5